## Slide 1
Chapter Seventeen
Introduction To Soft Computing And Fuzzy Logic

## Slide 2
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification 17.11 Defuzzification 17.12 Fuzzy Controllers
Learning Objectives
After reading this chapter, students would be able to:
• Understand the concept of soft computing and fuzzy logic
• Apply fundamental of fuzzy logic in the real-time application.

## Slide 3
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3 Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Introduction
Soft computing is the use of approximate calculations to produce in exact however usable solutions to complicated issues of machines. The approach allows solutions for the issues, which will either be unsolvable or too long to resolve with the current hardware. Typically, soft computing is termed as machine intelligence.
Soft computing provides associate in nursing approach to the problem-solving exploitation, which suggests that aside from the computers. With the human mind as a task model, soft computing is tolerant of partial truths, uncertainty, inexactness and approximation. It does not behave like the ancient computing models. The tolerance of soft computing permits researchers to approach some issues that ancient computing method cannot.
As a field of mathematical and PC study, soft computing has been around since the 1990s. The inspiration was the human mind’s ability to form real-world solutions to problems through approximation. Soft computing contrasts with the possibility, an approach that is used when there is not enough information available to solve a problem. In distinction, soft computing is used where the problem is not adequately specified for the use of conventional techniques of math and computer. Soft computing has varied real-world applications in domestic, industrial and industrial things.

## Slide 4: What is Soft Computing?
Soft Computing is a field that currently includes
Fuzzy Logic
Neural Networks
Probabilistic Reasoning(Genetic Algorithms, BBN), and
Other related methodologies
  Case-Based Reasoning
Soft Computing combines knowledge, techniques, and methodologies from the sources above to create intelligent systems
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3 Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers

## Slide 5: Why is this important?
The information revolution going on is allowing us to automate information processing tasks which require intelligence much like the industrial revolution automated manufacturing tasks
“Soft Computing” techniques have already been applied successfully.
Farming
corn & cows
Manufacturing
chairs & cars
Service
content and code
Industrial
Revolution
Information
Revolution
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3 Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 6: Soft Computing
“The essence of soft computing is that unlike the traditional, hard computing, soft computing is aimed at an accommodation with the pervasive imprecision of the real world. Thus, the guiding principle of soft computing is to exploit the tolerance for imprecision, uncertainty, and partial truth to achieve tractability, robustness, low solution cost, and better rapport with reality”
- Lotfi Zadeh
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3 Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 7
How does SC Relate to Other Fields
What is an Expert System (ES)?
User
Knowledge
Engineer
Knowledge
Acquisition
KB
rules
facts
Questions
Responses
Inference
Engine
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3 Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 8: How does SC relate to other fields?
AI
Soft Computing
Machine
Learning
symbolic
manipulation
uncertainty and imprecision
automatic
improvement
with
experience
Cognitive
Psychology
Study of the mind
Statistics
Probability
(not possibility)
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3 Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 9
Soft Computing Characteristics
Human Expertise (if-then rules, cases, conventional knowledge representations)
Biologically inspired computing models (NN)
New optimization techniques (GA, simulated annealing)
Model-free learning (NN, CBR)
Fault tolerance (deletion of neuron, rule, or case)
Real-world applications (large scale with uncertainties)
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3 Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 10
17.1 Introduction 17.2 Soft Computing Vs Hard Computing 17.3 Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Soft Computing Vs Hard Computing

## Slide 11
Various types of Soft Computing and Hard Computing Techniques
The principle techniques of soft computing include the following:
1.NeuraL Network
2.Fuzzy logic
3.Genetic Algorithm
1. Neural networks (NN)-NNs are the information processing systems that are inspired by the way of the biological nervous system and brain works. Typically, NNs area unit is designed for the specific applications, such as pattern recognition, data recognition, image processing, stock exchange prediction , weather prediction, image compression and security and loan applications. The aim of NN is to bring the normal computers a bit nearer to working of a human brain.
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3 Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers

## Slide 12
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3 Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
2. Fuzzy logic (FL)- The concept of fuzzy logic was introduced by Zade has a technique for representing human data that’s
imprecise by nature. The fuzzification interface transforms the crisp input worth into a fuzzy linguistic worth. The fuzzification is always necessary in an exceedingly mathematical logic system since the input values from the existing sensors are forever crisp numerical values.
Cont….
Various types of Soft Computing and Hard Computing Techniques

## Slide 13
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various Types Of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Various types of Soft Computing and Hard Computing Techniques
3.Genetic algorithms -are parts of the artificial intelligence and fuzzy computing. These are used mainly to solve various optimisation problems encountered in the real-life applications.
The basic processes in genetic algorithms are as follows:
1. Initialisation , where an initial population is created randomly.
2. Evaluation, where each member of the population is evaluated and the fitness of the individuals are
assessed on the basis of how well these match with the required needs.
3. Selection, where only the ones that fit the desired requirements are selected.
4. Crossover, where new individuals are created by combining the best aspects of the existing individuals.
At the end of this, it is expected to make people that square measure nearer to the required needs. The process is recurrent from the second step till a termination condition is reached finally.
Cont….

## Slide 14
Fuzzy Logic
Based on a system of non-digital (continuous & fuzzy without crisp boundaries) set theory and rules.
Developed by Lotfi Zadeh in 1965
Its advantage is its ability to deal with vague systems and its use of linguistic variables.
An accurate quantitative model is not required to control a plant or determine appropriate action.
Leads to faster and simpler program development of system controllers.
It can be a decision support system tool for managers
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 15
Fuzzy Logic Example
Automotive Speed Controller
3 inputs:
speed (5 levels)
acceleration (3 levels)
distance to destination (3 levels)
1 output:
power (fuel flow to engine)
Set of rules to determine output based on input values
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 16
Fuzzy Logic Example
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 17
Fuzzy Logic Example
Example Rules
IF speed is TOO SLOW and acceleration is DECELERATING,
THEN INCREASE POWER GREATLY
IF speed is SLOW and acceleration is DECREASING,
THEN INCREASE POWER SLIGHTLY
IF distance is CLOSE,
THEN DECREASE POWER SLIGHTLY
. . .
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 18
Output Determination
Degree of membership in an output fuzzy set now represents each fuzzy action.
Fuzzy actions are combined to form a system output.
Fuzzy Logic Example
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 19
Fuzzy Logic Example
Steps
Fuzzification: determines an input's % membership in overlapping sets.
Rules: determine outputs based on inputs and rules.
Combination/Defuzzification: combine all fuzzy actions into a single fuzzy action and transform the single fuzzy action into a crisp, executable system output. May use centroid of weighted sets.
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 20
Fuzzy Logic Example
Note there would be a total of 95 different rules for all combinations of inputs of 1, 2, or 3 at a time.
( 5x3x3 + 5x3 + 5x3 + 3x3 + 5 + 3 + 3 )
In practice, a system won't require all the rules.
System tweaked by adding or changing rules and by adjusting set boundaries.
System performance can be very good but not usually optimized by traditional metrics (minimize RMS error).
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 21
Classical Feedback Control
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 22: Modern Control
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 23: Model Reference Adaptive Control
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 24
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
The word fuzzy refers to things that are vague. Any event, process or function that is changing continuously cannot always be defined as either true or false. This implies that it is required to define such activities in a fuzzy manner.
Fuzzy logic resembles human decision-making methodology. It deals with vague and imprecise information. This is gross oversimplification of the real-world issues and supported degrees of the truth instead the usual true/false or 1/0 such as the mathematical logic.
Fuzzy Logic

## Slide 25
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Fuzzy Set versus Crisp Set
Cont….

## Slide 26
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic Introduction 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Fuzzy Set versus Crisp Set
Fuzzy set and crisp set are the part of the distinct set theories, where the fuzzy set implements infinite-valued logic while crisp set employs bivalued logic. Previously, professional system principles were developed premised on the mathematical logic wherever crisp sets area unit is used.
But then scientists argued that human thinking does not perpetually follow crisp “Yes”/”No” logic, and it may be well-obscure, qualitative, uncertain, general or fuzzy in nature. This gave commencement to the development of the fuzzy set theory to imitate human thinking.
For an element in a universe comprising fuzzy sets can have a progressive transition among several
degrees of membership. Whereas in the crisp sets the transition for an element in the universe between
membership and non-membership in a given set is sudden and well-defined.

## Slide 27
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Membership Function
We already apprehend that symbolic logic isn’t logic that is fuzzy. However, logic that is accustomed describes the blurriness. This blurriness is best characterised by its membership operate. Alternatively, it can be said that membership operate represents the degree of truth in symbolic logic (Figure 17.2).
                Contd…

## Slide 28
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Membership Function
Following are many small prints about the membership operate:
1. Membership functions were first introduced in 1965 by Lofti A.
2. Zadeh in his first research paper wrote about the “Fuzzy sets”.
3. Membership functions characterise blurriness (i.e., all the data in fuzzy set), whether or not the weather in fuzzy sets are separate or continuous.
4. Membership functions will be outlined as a way to unravel sensible issues by expertise instead of information.
5. Membership functions are represented by graphical forms.
6. Rules for defining fuzziness are fuzzy too.

## Slide 29
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic Introduction
17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Fuzzy Rules
The power and flexibility of simple IF–THEN–ELSE logic rule is enhanced by adding linguistic parameter.
Fuzzy rules are expressed in the following form:
17.7.1 IF Variable IS Set THEN Action
Example:
1. IF temperature is very cold THEN switch off the air conditioner.
2. IF temperature is normal THEN adjust the air conditioner.
3. IF temperature is hot THEN switch on the air conditioner.
17.7.2 Interpretation of Fuzzy IF–THEN Rule
Fuzzy IF–THEN rules can be interpreted in following four ways:
Contd…

## Slide 30
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic
17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Fuzzy Rules
17.7.2.1 Assignment Statements
These kinds of statements use “=” (equal to sign) for the purpose of assignment. These are of the following form:
a = hello
climate = summer
17.7.2.2 Conditional Statements
These kinds of statements use the “IF–THEN” rule base form for the purpose of condition. These are of the following forms:
IF temperature is high THEN Climate is hot
IF food is fresh THEN eat.
                Contd…

## Slide 31
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic
17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Fuzzy Rules
17.7.2.3 Unconditional Statements
These are of the following form:
GOTO 10
turn the Fan off
17.7.2.4 Linguistic Variables
We have studied that formal logic uses linguistic variables that square measure the words or sentences in a very tongue. For example, if we say temperature, it is a linguistic variable; the values of which are very hot or cold, slightly hot or cold, very warm, slightly warm, etc. The words very, slightly are the linguistic hedges.
17.7.2.5 Characterisation of Linguistic Variable
Following four terms characterise the linguistic variable:
1. Name of the variable, generally represented by x.
2. Term set of the variable, generally represented by t(x).
3. Syntactic rules for generating the values of the variable x.
4. Semantic rules for linking each price of x and its significance.

## Slide 32
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification 17.11 Defuzzification 17.12 Fuzzy Controllers
Fuzzy Reasoning
17.8.1 Categorical Reasoning
In this mode of approximate reasoning, the antecedents, containing no fuzzy quantifiers and fuzzy chances,
square measure assumed to be in canonical kind.
17.8.2 Qualitative Reasoning
In this mode of approximate reasoning, the antecedents and consequents have fuzzy linguistic variables; the
input–output relationship of a system is expressed as a collection of fuzzy IF–THEN rules. This reasoning
is mainly used in control system analysis.
Contd…

## Slide 33
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules
17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification 17.11 Defuzzification 17.12 Fuzzy Controllers
Fuzzy Reasoning
17.8.3 Syllogistic Reasoning
In this mode of approximation reasoning, antecedents with fuzzy quantifiers are related to inference rules.
This is expressed as:
Here A,B,C,D,E,F are the fuzzy predicates
S1 and S2 are given fuzzy quatifier and S3 is the fuzzy quantifier to be decided.
17.8.4Dispositional Reasoning
In this mode of approximation reasoning, the antecedents are dispositions that may contain fuzzy quantifier “usually”. The quantifier “usually” links together dispositional and syllogistic reasoning. Hence it plays an important role. For example, the projection rule of inference in dispositional reasoning can be given as: usually((L,M) is R) 33→usually (L is [R↓L])
.

## Slide 34
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification 17.11 Defuzzification 17.12 Fuzzy Controllers
Fuzzy Inference System
Fuzzy inference system is the key unit of a fuzzy logic system having decision making as its primary work . It uses the “IF–THEN” rules along with connectors “OR” or “AND” for drawing essential decision rules.
17.9.1 Characteristic of Fuzzy Inference System
Following are some characteristics of the fuzzy interference system (FIS):
1. The output from FIS is always a fuzzy set irrespective of its input, which can be fuzzy or crisp.
2. It is necessary to own fuzzy output once it is used as a controller.
3. A defuzzification unit would be there with FIS to convert fuzzy variables into crisp variables.

## Slide 35
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification 17.11 Defuzzification 17.12 Fuzzy Controllers
Fuzzy Inference System
17.9.2 Function Block of FIS
17.9.3 Working Of FIS- The working of FIS consists of following steps:
1. A fuzzification unit supports the appliance of various fuzzification strategies, and converts the crisp
input into fuzzy input.
2. A mental object: Assortment of rule base and information is made upon the conversion of crisp input
into fuzzy input.
The defuzzification unit fuzzy input is finally reborn into crisp output.

## Slide 36
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 1.10 Fuzzification 17.11 Defuzzification 17.12 Fuzzy Controllers
Fuzzification
It may be outlined because the method of remodelling a crisp set to a fuzzy set or a fuzzy set to fuzzier
set. Basically, this operation interprets correct crisp input values into linguistic variables. Following square
measure the two vital ways of fuzzification
17.10.1 Support Fuzzification (s-fuzzification) Method-
In this methodology, the fuzzified set will be expressed with the assistance of the subsequent relation:
Ã=μ1Q(x1)+μ2 Q(x2)+…+ μn Q(x n)
Here, the fuzzy set Q(xi) is called kernel of fuzzification. This method is implemented by keeping μi constant and xi being transformed to a fuzzy set Q(xi) Q(xi).
17.10.2 Grade Fuzzification Method
Grade fuzzification method is quite similar to the aforementioned method but the main difference is that it kept xi constant and μi is expressed as a fuzzy set. Cont….

## Slide 37
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification 17.12 Fuzzy Controllers
Defuzzification
Defuzzification may be outlined because the method of reducing a fuzzy set into a crisp set or to convert a fuzzy member into a crisp member. We have already studied that the fuzzification method involves conversion from crisp quantities to fuzzy quantities.
In a variety of engineering applications, it is necessary to defuzzify the result or rather “fuzzy result” so it should be regenerate to crisp result. Mathematically, the method of defuzzification is additionally known as “rounding it off”. The different strategies of defuzzification are represented below:
17.11.1Max-Membership Method- Max–membership method technique is restricted to peak output functions and conjointly known as height technique.
17.11.2 Max-Mean Membership Method- This method is limited to peak output functions and also known as height method. Mathematically, it can
be represented as follows:
μÃ (x*)> μÃ (x) for all x є X
Here x* is defuzzified output

## Slide 38
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification 17.11 Defuzzification 17.11 Defuzzification 17.12 Fuzzy Controllers
Defuzzification
17.11.3 Centroid Method-This method is also known as the centre of area or the centre of gravity method. Mathematically, the defuzzified output x* will be represented as:
17.11.4 Weighted Average Method - In this method, each membership function is weighted by its maximum membership value. Mathematically, the defuzzified output x* will be represented as:
Contd…

## Slide 39
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification 17.11 Defuzzification 17.12 Fuzzy Controllers
Defuzzification
17.11.5 Mean-Max Method - This method is also known as the middle of the maxima. Mathematically, the defuzzified output x* will be represented as:

## Slide 40
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function 17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification 17.11 Defuzzification
17.12 Fuzzy Controllers
Fuzzy Controllers
Adaptive fuzzy controller is meant with some adjustable parameters beside associate degree embedded mechanism for adjusting them. Adaptive controller has been used for the performance of controller.
17.12.1 Basic Steps for Implementing Adaptive Algorithm
1. Collection of observable data
2. Adjustment of controller parameters
3. Improvement in performance of controller
17.12.2 Operational Concepts

## Slide 41
Fuzzy Logic Summary
Doesn't require an understanding of process but any knowledge will help formulate rules.
Complicated systems may require several iterations to find a set of rules resulting in a stable system.
Combining Neural Networks with fuzzy logic reduces time to establish rules by analyzing clusters of data.
Possible applications: Master Production Schedule, Material Requirements Planning, Inventory Capacity Planning
17.1 Introduction 17.2 Soft Computing versus Hard Computing 17.3Various types of Soft Computing and Hard Computing Techniques 17.4 Fuzzy Logic 17.5 Fuzzy Set versus Crisp Set 17.6 Membership Function
17.7 Fuzzy Rules 17.8 Fuzzy Reasoning 17.9 Fuzzy Inference System 17.10 Fuzzification
17.11 Defuzzification
17.12 Fuzzy Controllers
Copyright © 2019 by Wiley India Pvt. Ltd., 4436/7, Ansari Road, Daryaganj, New Delhi-110002

## Slide 42
Dr. Nilakshi Jain Email ID : nilakshijain1986@gmail.com
Thank you